## Slide 2: Intro to Multiprocessor Programming

## Slide 3: Administrative
Ming Fu fuming@ustc.edu.cn
Homepage http://home.ustc.edu.cn/~fuming
Research Interests :
  Concurrency Theory
  Concurrency Verification
Phone(O) : 87161326

## Slide 4: Requirements
Assignments (40%)
  Homework and Programming
Final exam (60%)

## Slide 5: Moore’s Law
5
Clock speed flattening sharply
Transistor count still rising
Notes: 5
Most of you have probably heard of Moore’s law, which states that the number of transistors on a chip tends to double about every two years. Moore’s law has been the engine of growth for our field, and the reason you can buy a laptop for a few thousand dollars that would have cost millions a decade earlier. The green dots on this graph show

## Slide 6: Vanishing from your Desktops: The Uniprocesor
6
memory
cpu
Notes: 6
Traditionally, we have had inexpensive single processor with an associated memory on a chip, which we call a uniprocessor.

## Slide 7: Your Server: The Shared Memory Multiprocessor (SMP)
7
cache
Bus
Bus
shared memory
cache
cache
Notes: 7
And we had expensive multiprocessor chips in the enterprise, that is, in server farms, high performance computing centers and so on. The
Shared memory multiprocessor (SMP) consists of multiple CPUs connected by a bus or interconnect network to a shared memory.

## Slide 8: Your New Server or Desktop: The Multicore Processor (CMP)
8
cache
Bus
Bus
shared memory
cache
cache
All on the
same chip
Sun T2000
Niagara
Notes: 8
The revolution we are going through is that the desktop is now becoming a multiprocessor also. We call this type of processor a system-on-a-chip or a multicore machine or a chip multiprocessor (CMP). The chip you see here is the Sun T2000 Niagara CMP that has 8 cores and shared cache and memory. We will learn about the Niagara in more detail later. It is the machine you will be using for your homework assignments.

## Slide 9: From the 2008 press…
9
…Intel has announced a press conference in San Francisco on November 17th, where it will officially launch the Core i7 Nehalem processor…
…Sun’s next generation Enterprise T5140 and T5240 servers, based on the 3rd Generation UltraSPARC T2 Plus processor, were released two days ago…
Notes: 9
In 1994, Intel made a quiet announcement that is going to have profound consequences for everyone who uses computers. The long-term importance of this news is only slowly being appreciated. Essentially, Intel stated that they have given up trying to make the Pentium processor, their flagship product run faster. They didn’t actually say why, but the word on the street is that they overheat. This is a substantial change from the way the field has worked from the very beginning.

## Slide 10
10
Why is Kunle Smiling?
Niagara 1
Notes: Cause he doesn’t have to write the software…
10

## Slide 11: Why do we care?
11
Time no longer cures software bloat
  The “free ride” is over
When you double your program’s path length
  You can’t just wait 6 months
  Your software must somehow exploit twice as much parallelism or concurrency
Notes: 11
Why do you care? Because the way you wrote software until now will disappear in the next few years. The free ride where you write software once and trust Intel, Sun, IBM, and AMD to make it faster is no longer valid.

## Slide 12: A simplified view of history
Writing correct and efficient multithreaded code is often much more difficult than for single-threaded (i.e., sequential) code
  Especially in common languages like Java and C
  So typically stay sequential if possible
From roughly 1980-2005, desktop computers got exponentially faster at running sequential programs
  About twice as fast every couple years
But nobody knows how to continue this
  Increasing clock rate generates too much heat
  Relative cost of memory access is too high
  But we can keep making “wires exponentially smaller” (Moore’s “Law”), so put multiple processors on the same chip (“multicore”)

## Slide 13: Traditional Scaling Process
13
User code
Traditional
Uniprocessor
Speedup
1.8x
7x
3.6x
Time: Moore’s law
Notes: 13
Recall the traditional scaling process for software: write it once, trust Intel to make the CPU faster to improve performance.

## Slide 14: Multicore Scaling Process
14
User code
Multicore
Speedup
1.8x
7x
3.6x
Unfortunately, not so simple…
Notes: 14
With multicores, we will have to parallelize the code to make software faster, and we cannot do this automatically (except in a limited way on the level of individual instructions).

## Slide 15: Real-World Scaling Process
15
1.8x
2x
2.9x
User code
Multicore
Speedup
Parallelization and Synchronization
require great care…
Notes: 15
This is because splitting the application up to utilize the cores is not simple, and coordination among the various code parts requires care.

## Slide 16: Multiprocessor Programming: Course Overview
16
Fork-Join Parallel programming
Basic Principles of Concurrency
Concurrent Data Structures
Notes: 16
Here is our course overview. (at the end, we aim to give you a basic understanding of the issues, not to make you exerts) [[Lecturer can tell
Mongolian Expert on the Montain Joke]].
In this course, we will study a variety of synchronization algorithms,
with an emphasis on informal reasoning about correctness.
Reasoning about multiprocessor programs is different in many ways from the more
familiar style of reasoning about sequential programs.
Sequential correctness is mostly concerned with safety properties,
that is, ensuing that a program transforms each before-state to the correct
after-state.
Naturally, concurrent correctness is also concerned with safety,
but the problem is much, much harder,
because safety must be ensured despite the vast number of ways steps of
concurrent threads can be be interleaved.
Equally important, concurrent correctness encompasses a variety of
\emph{liveness} properties that have no counterparts in the sequential world.
The second part of the book concerns performance.
Analyzing the performance of synchronization algorithms is also different
in flavor from analyzing the performance of sequential programs.
Sequential programming is based on a collection of well-established and
well-understood abstractions.
When you write a sequential program,
you usually do not need to be aware that underneath it all,
pages are being swapped from disk to memory,
and smaller units of memory are being moved in and out of a hierarchy of
processor caches.
This complex memory hierarchy is essentially invisible,
hiding behind a simple programming abstraction.
In the multiprocessor context, this abstraction breaks down,
at least from a performance perspective.
To achieve adequate performance,
the programmer must sometimes ``outwit'' the underlying memory system,
writing programs that would seem bizarre to someone unfamiliar with
multiprocessor architectures.
Someday, perhaps, concurrent architectures will provide the same degree of
efficient abstraction now provided by sequential architectures,
but in the meantime, programmers should beware.
We start then with fundamentals, trying to understand what is and is not computable before we try and write programs. This is similar to the process you have probably gone through with sequential computation of learning computability and complexity theory so that you will not try and solve unsolvable problems. There are many such computational pitfals when programming multiprocessors.

## Slide 17: Sequential Computation
17
memory
object
object
thread
Notes: 17

## Slide 18: Parallel or Concurrent Computation
18
memory
object
object
threads
Notes: 18

## Slide 19: Asynchrony
19
Sudden unpredictable delays
  Cache misses (short)
  Page faults (long)
  Scheduling quantum used up (really long)
Notes: 19

## Slide 20: Serial Vs. Parallel
Q
Please
COUNTER
COUNTER 1
COUNTER 2

## Slide 21: High Performance Computing
Parallel Machine : MPP
function1( )
{
//......function stuff
}
function2( )
{
//......function stuff
}
Serial Machine
function1 ( ):
function2 ( ):
Single CPU
Time : add (t1, t2)
function1( ) || function2 ( )
massively parallel system
containing thousands of CPUs
Time : max (t1, t2)
t1
t2

## Slide 22: Parallelism vs. Concurrency
Note: Terms not yet standard but the perspective is essential
  Many programmers confuse these concepts
There is some connection:
  Common to use threads for both
  If parallel computations need access to shared resources, then the concurrency needs to be managed
First some lectures on parallelism, then some lectures on concurrency
Parallelism:
Use extra resources to
solve a problem faster
resources
Concurrency:
Correctly and efficiently manage
access to shared resources
requests
work
resource

## Slide 23: An analogy
CS1 idea: A program is like a recipe for a cook
  One cook who does one thing at a time! (Sequential)
Parallelism:
  Have lots of potatoes to slice?
  Hire helpers, hand out potatoes and knives
  But too many chefs and you spend all your time coordinating
Concurrency:
  Lots of cooks making different things, but only 4 stove burners
  Want to allow access to all 4 burners, but not cause spills or incorrect burner settings

## Slide 24: Parallelism Example
Parallelism: Use extra computational resources to solve a problem faster (increasing throughput via simultaneous execution)
Pseudocode for array sum
  Bad style for reasons we’ll see, but may get roughly 4x speedup
int sum(int[] arr){
res = new int[4];
len = arr.length;
FORALL(i=0; i < 4; i++) { //parallel iterations
res[i] = sumRange(arr,i*len/4,(i+1)*len/4);
}
return res[0]+res[1]+res[2]+res[3];
}
int sumRange(int[] arr, int lo, int hi) {
result = 0;
for(j=lo; j < hi; j++)
result += arr[j];
return result;
}

## Slide 25: Concurrency Example
Concurrency: Correctly and efficiently manage access to shared resources (from multiple possibly-simultaneous clients)
Pseudocode for a shared chaining hashtable
  Prevent bad interleavings (correctness)
  But allow some concurrent access (performance)
class Hashtable<K,V> {
…
void insert(K key, V value) {
int bucket = …;
prevent-other-inserts/lookups in table[bucket]
do the insertion
re-enable access to arr[bucket]
}
V lookup(K key) {
(like insert, but can allow concurrent
lookups to same bucket)
}
}

## Slide 26: Model Summary
26
Multiple threads
  Sometimes called processes
Single shared memory
Objects live in memory
Unpredictable asynchronous delays
Notes: 26

## Slide 27: Shared memory
The model we will assume is shared memory with explicit threads
Old story: A running program has
  One call stack (with each stack frame holding local variables)
  One program counter (current statement executing)
  Static fields
  Objects (created by new) in the heap (nothing to do with heap data structure)
New story:
  A set of threads, each with its own call stack & program counter
    No access to another thread’s local variables
  Threads can (implicitly) share static fields / objects
    To communicate, write somewhere another thread reads

## Slide 28: Shared memory
Threads each have own unshared call stack and current statement
  (pc for “program counter”)
  local variables are numbers, null, or heap references
Any objects can be shared, but most are not
…
pc=…
…
pc=…
…
pc=…
…
Unshared:
locals and
control
Shared:
objects and
static fields

## Slide 29: Other models
We will focus on shared memory, but you should know several other models exist and have their own advantages
Message-passing: Each thread has its own collection of objects. Communication is via explicitly sending/receiving messages
  Cooks working in separate kitchens, mail around ingredients
Dataflow: Programmers write programs in terms of a DAG.
A node executes after all of its predecessors in the graph
  Cooks wait to be handed results of previous steps
Data parallelism: Have primitives for things like “apply function to every element of an array in parallel”

## Slide 30: Our Needs
To write a shared-memory parallel (concurrent) programs, need new primitives from a programming language or library
Ways to create and run multiple things at once
  Let’s call these things threads
Ways for threads to share memory
  Often just have threads with references to the same objects
Ways for threads to coordinate (a.k.a. synchronize)
  For now, a way for one thread to wait for another to finish
  Other primitives when we study concurrency

## Slide 31: Few Popular Thread Models
POSIX, ISO/IEEE standard
Mach C threads, CMU
Sun OS LWP threads, Sun Microsystems
PARAS CORE threads, C-DAC
Java-Threads, Sun Microsystems
Chorus threads, Paris
OS/2 threads, IBM
Windows NT/95 threads, Microsoft

## Slide 32: Intro to Java-Threads

## Slide 33: Java Threads
Resources
  Java Threads by Scott Oaks & Henry Wong (O’Reilly)
  API docs
    http://download.oracle.com/javase/6/docs/api/
      java.lang.Thread, java.lang.Runnable
      java.lang.Object, java.util.concurrent
  Tutorials
    http://download.oracle.com/javase/tutorial/essential/concurrency/index.html
    http://download.oracle.com/javase/tutorial/essential/concurrency/procthread.html
  Introduction to Java Threads
    http://www.javaworld.com/javaworld/jw-04-1996/jw-04-threads.html
  Thread safety
    http://en.wikipedia.org/wiki/Thread-safety
    http://www.javaworld.com/jw-08-1998/jw-08-techniques.html
Notes: Contrast between a class with synchronization and a class without synchronization!! How many threads can call the methods at the same time on an instance?

## Slide 34: Coverage
Thread class
  run, start methods
  yield, join
  sleep
Synchronization
  synchronized methods & objects
  wait/notify/notifyAll
  conditions
Notes: Next time add Java Conditions into this in synchronization part
http://java.sun.com/j2se/1.5.0/docs/api/java/util/concurrent/locks/Condition.html

## Slide 35: Ways of Multithreading in Java
Create a class that extends the Thread class
Create a class that implements the Runnable interface
1st Method: Extending the Thread class
class MyThread extends Thread
{
public void run()
{
// thread body of execution
}
}
Creating thread : MyThread thr1 = new MyThread();
Start Execution: thr1.start();

## Slide 36: 2nd method: Threads by implementing Runnable interface
class ClassName implements Runnable
{
.....
public void run()
{
// thread body of execution
}
}
Creating Object:
ClassName myObject = new ClassName();
Creating Thread Object:
Thread thr1 = new Thread( myObject );
Start Execution: thr1.start();

## Slide 37: Thread Class Members...
public class java.lang.Thread extends java.lang.Object
implements java.lang.Runnable
{
// Fields
public final static int MAX_PRIORITY;
public final static int MIN_PRIORITY;
public final static int NORM_PRIORITY;
// Constructors
public Thread();
public Thread(Runnable target);
public Thread(Runnable target, String name);
public Thread(String name);
public Thread(ThreadGroup group, Runnable target);
public Thread(ThreadGroup group, Runnable target, String name);
public Thread(ThreadGroup group, String name);
// Methods
public static int activeCount();
public void checkAccess();
public int countStackFrames();
public static Thread currentThread();
public void destroy();
public static void dumpStack();
public static int enumerate(Thread tarray[]);
public final String getName();

## Slide 38: ...Thread Class Members.
public final int getPriority(); // 1 to 10 priority-pre-emption at mid.
public final ThreadGroup getThreadGroup();
public void interrupt();
public static boolean interrupted();
public final boolean isAlive();
public final boolean isDaemon();
public boolean isInterrupted();
public final void join();
public final void join(long millis);
public final void join(long millis, int nanos);
public final void resume();
public void run();
public final void setDaemon(boolean on);
public final void setName(String name);
public final void setPriority(int newPriority);
public static void sleep(long millis);
public static void sleep(long millis, int nanos);
public void start();
public final void stop();
public final void stop(Throwable obj);
public final void suspend();
public String toString();
public static void yield();
}

## Slide 39: Example 1: Manipulation of Current Thread
// CurrentThreadDemo.java
class CurrentThreadDemo {
public static void main(String arg[]) {
Thread ct = Thread.currentThread();
ct.setName( "My Thread" );
System.out.println("Current Thread : "+ct);
try {
for(int i=5; i>0; i--) {
System.out.println(" " + i);
Thread.sleep(1000);
}
}
catch(InterruptedException e) {
System.out.println("Interrupted."); }
}
}
Run:
Current Thread : Thread[My Thread,5,main]
5
4
3
2
1

## Slide 40: Example2 :Creating new Thread...
// ThreadDemo.java
class ThreadDemo implements Runnable
{
ThreadDemo()
{
Thread ct = Thread.currentThread();
System.out.println("Current Thread : "+ct);
Thread t = new Thread(this,"Demo Thread");
t.start();
try
{
Thread.sleep(3000);
}
catch(InterruptedException e)
{
System.out.println("Interrupted.");
}
System.out.println("Exiting main thread.");
}

## Slide 41: Example2 :Creating new Thread.
public void run() {
try {
for(int i=5; i>0; i--) {
System.out.println(" " + i);
Thread.sleep(1000);
} }
catch(InterruptedException e) {
System.out.println("Child interrupted.");
}
System.out.println("Exiting child thread.");
}
public static void main(String args[]) {
new ThreadDemo();
}
}
Run:
Current Thread : Thread[main,5,main]
5
4
3
Exiting main thread.
2
1
Exiting child thread.

## Slide 42: Example 3
Create 2 threads from the Main, then start them
Threads will be instances of different thread sub-classes

## Slide 43
class MyThreadA extends Thread {
public void run() { // entry point for thread
for (;;) {
System.out.println("hello world1");
}
}
}
class MyThreadB extends Thread {
public void run() { // entry point for thread
for (;;) {
System.out.println("hello world2");
}
}
}
public class Main1 {
public static void main(String [] args) {
MyThreadA t1 = new MyThreadA();
MyThreadB t2 = new MyThreadB();
t1.start();
t2.start();
// main terminates, but in Java the other threads keep running
// and hence Java program continues running
}
}

## Slide 44
hello world2
hello world2
hello world1
hello world2
hello world1
hello world2
hello world2
hello world1
hello world1
hello world1
hello world1
hello world2
hello world1
hello world1
hello world2
hello world2
hello world1
hello world1
hello world2
hello world2
hello world1
hello world1
hello world2
Notes: Run on Mac OS X, 3/14/08
Sometimes in multithreaded programs, you see parts of the output more interspersed than this.

## Slide 45: Example 4
Create 2 threads from the Main, then start them
Threads will be instances of the same thread sub-class
Use argument of constructor of new thread class to pass text name of thread, e.g., “thread1” and “thread2”
  Data member provides different data per thread (i.e., then name)
  A data member can also be used to share data
Notes: Have the students work this example.

## Slide 46
class MyThread extends Thread {
private String name;
public MyThread(String name) {
this.name = name;
}
public void run() {
for (;;) {
System.out.println(name + ": hello world");
}
}
}
public class Main2 {
public static void main(String [] args) {
MyThread t1 = new MyThread("thread1");
MyThread t2 = new MyThread("thread2");
t1.start(); t2.start();
}
}

## Slide 47
thread2: hello world
thread2: hello world
thread2: hello world
thread2: hello world
thread2: hello world
thread2: hello world
thread2: hello world
thread2: hello world
thread2: hello world
thread2: hello world
thread2: hello world
thread2: hello world
thread2: hello world
thread2: hello world
thread2: hello world
thread1: hello world
thread2: hello world
thread1: hello world
thread2: hello world
thread2: hello world
thread1: hello world
thread2: hello world
thread2: hello world
Notes: See the variation in output.

## Slide 48: java.lang.Thread
public static void yield();
  Method of java.lang.Thread
  Thread gives up CPU for other threads ready to run

## Slide 49
class MyThread extends Thread {
private String name;
public MyThread(String name) {
this.name = name;
}
public void run() {
for (;;) {
System.out.println(name + ": hello world");
yield();
}
}
}
public class Main3 {
public static void main(String [] args) {
MyThread t1 = new MyThread("thread1");
MyThread t2 = new MyThread("thread2");
t1.start(); t2.start();
}
}

## Slide 50: Some Output
thread1: hello world
thread2: hello world
thread1: hello world
thread2: hello world
thread1: hello world
thread2: hello world
thread1: hello world
thread2: hello world
thread1: hello world
thread2: hello world
thread1: hello world
thread2: hello world
thread1: hello world
thread2: hello world
thread1: hello world
thread2: hello world
thread1: hello world
thread2: hello world
thread1: hello world
thread2: hello world
thread1: hello world
thread2: hello world
thread1: hello world
Notice the alternation of output
Notes: Run on Mac OS X, 3/14/08

## Slide 51: More Thread Members: join
public final void join();
  MyThread t1 = new MyThread("thread1");
  t1.start();
  t1.join();
  Wait until the thread is “not alive”
  Threads that have completed are “not alive” as are threads that have not yet been started
public static void sleep (long millis) throws InterruptedException;
  Makes the currently running thread sleep (block) for a period of time
  The thread does not lose ownership of any monitors.
  InterruptedException - if another thread has interrupted the current thread.
Notes: final on a method indicates it can’t be overridden

## Slide 52: Join Example

## Slide 53: Some output
…
hello world1
hello world1
hello world1
hello world1
hello world1
hello world1
hello world1
hello world1
hello world1
hello world1
hello world1
hello world1
hello world1
hello world1
hello world1
hello world1
hello world1
hello world1
hello world1
hello world1
hello world1
Thread is done!

## Slide 54: Sharing Data Across Java Threads
Consider the situation where a parent thread wants to pass data to a child thread
  e.g., so that child can change data and parent can have access to the changed data
How can this be done?
Can pass an object instance to the child thread constructor, and retain that object instance in a data member

## Slide 55
class SharedData {
public int a = 0;
public String s = null;
public SharedData() {
a = 10;
s = "Test";
}
}
class MyThread extends Thread {
private SharedData m_data = null;
public MyThread(SharedData data) {
m_data = data;
}
public void run() {
for (;;) {
m_data.a++;
}
}
}

## Slide 56
public class Main5 {
public static void main(String [] args) {
SharedData data = new SharedData();
MyThread t1 = new MyThread(data);
t1.start();
for (;;) {
data.a--;
}
}
}
If we have multiple threads accessing this shared data, how do we synchronize access to ensure it remains in a consistent state?
Notes: Of course, part of this depends on how we define “consistent state”.

## Slide 57: Basic Tools for Synchronization in Java
Synchronized methods
Synchronized objects
Methods
  wait
  notify
  notifyAll
Also should talk about condition variables in Java

## Slide 58: Synchronized Methods: Monitors
synchronized keyword used with a method
  E.g.,
    public synchronized void SetValue() {
    // Update instance data structure.
    // When the thread executes here, it exclusively has the monitor lock
    }
  Provides instance-based mutual exclusion
    A lock is implicitly provided-- allows at most one thread to be executing the method at one time
  Used on a per method basis; not all methods in a class have to have this
    But, you’ll need to design it right!!